Although we at USR cannot provide the dialers to you directly, SCO has
 provided us the following document detailing how to download them from SCO.


 How to download Support Level Supplements, such as the high speed dialers
 for the USRobotics High Speed Modems, using UUCP.

 KEYWORDS: downloading uucp transfer support level supplements sls sosco bbs
 xenix

 RELEASE: SCO UNIX system V Operating System Generic

 PROBLEM: Is there a way to get the supplements (EFS) using UUCP rather than
 ordering them on diskette?

 SOLUTION: Selected supplements (EFS) are available for transfer using UUCP.
 This service is available to any SCO customer regardless of support status.
 To use this service, you should be familiar with setting up and using UUCP
 as described in the chapter "Building a Remote Network with UUCP: in the
 SCO XENIX System Administrator's Guide.

 Before attempting to transfer an EFS file, you must have a modem configured
 to dial out from your computer. For more information on configuring a
 modem, see chapter 14, "Using Terminals and Modems:, in the Systems
 Administrator's Guide.

 Once you have your modem configured for dialing out, you must set up your
 UUCP configuration to recognize the SCO system which contains the EFSs. If
 you have a 2400 baud or lower modem, add the following line to the end of
 the "Systems" configuration file in the directory /usr/lib/uucp:

 sosco Any ACU 2400 14084253502 ogin:-@-ogin:-@-ogin: uuefs
                                                      or
                                                     uusls

 Once your system is configured, you can use the uucp(C) command to request
 files from the remote system. All files reside in the directory
 /usr/spool/uucppublic/EFS. The uucp(C) command to transfer these files into
 the directory /usr/spool/uucppublic on your system is:

 uucp sosco! /usr/spool/uucppublic/EFS/efs111.z /usr/spool/uucppublic
 /efs111.z

 uucp sosco! /usr/spool/uucppublic/EFS/efs111.ltr /usr/spool/uucppublic
 /efs111.ltr

 If you are using the C shell command interpreter, you must enter a
 backslash character "\" before the exclamation mark "!" to prevent the C
 shell history mechanism from intercepting the rest of the command line.

 The ".ltr" file contains the names of all the other files that are
 available and instructions on how to install the EFSs once they have been
 transfered to your system.